Table 1 Bicycle lane regulations, measurements and application criteria

|  | Germany | Switzerland | Denmark |
| --- | --- | --- | --- |
| name | Radfahrstreife | Schutzstreife (also Suggestivstreife, Radspur, Angebotstreife) | Radstreife | Kernfahrbahn | Cykelbaner |
| signposting | white, continuous, 25 cm wide | white, interrupted (1-1), 12 cm wide | yellow, interrupted (3-3) or continuous, 20 cm wide | yellow, interrupted (3-3) | white, continuous, 30 cm |
| width | standard 1.85 m, minimum 1.50 m | standard 1.60 m, minimum 1.25 m | minimum 1.20 m | minimum 1.20 m | standard 1.50 m, minimum 1.20 m |
| use | - cyclists (obligatory), - all others prohibited | - cyclists (obligatory) - may be left to pass cyclists - may be used by others if needed | - cyclists (obligatory) - may be used by others if needed, at interrupted line | - cyclists (obligatory) - may be used by others if needed, at interrupted line | - cyclists (obligatory), - all others prohibited |
| prerequisite | - lane width ≥9.00 m - max. 18,000 veh/24h (2 lanes) and 25,000 (4 lanes) | - lane width ≥7.00 m, <8.50 m - motor veh. lane min. 4.50m, max. 5.50 m - max. 10,000 veh/24h - <5% lorries |  | single lane for 2-way car traffic, no axis marked, < 6 m wide between bicycle lanes |  |